## Slide 1: Small Antennas – Part 2
Slot antennas
Yagi antennas
Log-periodic wideband antennas
Microstrip patch antennas
Inverted F-antennas
Planar Inverted F-antennas
Miniaturization
Dr. Rob Maaskant

## Slide 2: Learning Goals
Describe the function of the elements in a Yagi antenna
Explain the design philosophy of a log-periodic antenna
Describe the main difference between a normal log-periodic antenna and the log-periodic eleven antenna
Explain how to feed a rectangular patch antenna for linear, dual and circular polarizations
Describe the dual slot model for the radiation field function for a rectangular patch antenna on a thin substrate
Apply design curves and formulas for the design of rectangular patch antennas

## Slide 3: Slot antennas
Undesired slots in shields:
  Electromagnetic compatibility (EMC) problems
  Antenna measurement chambers often shielded
Desired slots (slot antennas):
  Fed by waveguides
  Linear array
  Planar array antenna
  Cheap to manufacture
  Very accurate numerical models

## Slide 4: Slot: Field distribution
Slot resembles a short rectangular waveguide, with basic TE10 mode field. Therefore, the field distribution over a slot is:
  Good approximation even for thin wall
  Not effected much by type of excitation
  Not effected much by form and shape of ground plate

## Slide 5: Slot: Radiation function using equivalent magnetic sources
E
0
m
E
s
l
o
t
z
ˆ
´
E
0
p
x'
l
¤
(
)
x
ˆ
cos
=
=

## Slide 6: Slot: Radiation function
Incremental magnetic source factor:
Fourier transform factor:
Radiation function:
Excitation:
Radiation function consists of 3 parts:

## Slide 7: Slot: Radiation function
Directivity 3 dB larger than dipole

## Slide 8: Comparison
Dipole
z
x
y

## Slide 9: Yagi-Uda antenna
A unidirectional (one direction only) antenna commonly used in communications for frequencies above 10 MHz
Commonly used as TV antenna
Now gain more attention at 60 GHz and above to THz.

## Slide 10: Basic configuration of Yagi
Driven element
  a center-fed, half-wave dipole.
Reflector
  behind driven element.
  slightly longer than driven element.
Directors
  in front of driven element.
  shorter than driven element.
  typically one reflector and several directors.
Reflector
Driven element
Directors
Here F =300/λ

## Slide 11: Typical radiation pattern of Yagi

## Slide 12: Characteristics of Yagi-Uda Antenna
End-fire antenna, not an aperture antenna
E-plane pattern and H-plane pattern are similar
  Even the E-plane and H-plane are very different in size
The gain does not increase linearly with the number of elements used.
  3-element Yagi has 5 to 6 dBi directivity.
  Adding another director results in a 2 dB increase.
  Additional directors have less and less effect.
  Adding more reflector has negligible effect.

## Slide 13: Yagi – Gain as a function of number of elements
From Stutzman, Thiele, Antenna theory and design

## Slide 14: Small Antennas – Part 2
Yagi antennas
Log-periodic wideband antennas
Microstrip patch antennas
Inverted F-antennas
Planar Inverted F-antennas
Miniaturization

## Slide 15: Log-Periodic Dipole Array (LPDA)
Phase centre location varies with frequency
Scale factor:

## Slide 16
Two parallel dipoles over ground (Eleven configuration)
  equal E- and H-plane patterns
  Beamwidth constant with frequency
  phase center is locked to the ground plane
  low far-out sidelobes and backlobes.
Decade bandwidth by
  Logperiodic
  Folded dipoles
Eleven Antenna – a decade bandwidth log-periodic antenna

## Slide 17
Several Projects on Eleven Antenna
For use in Green Bank
radio telescope for 150 – 1700 MHz
For use in RATAN telescope
for 500 – 3000 MHz
GMRT
for 200 – 800 MHz

## Slide 18
Measured Radiation Patterns in 45 deg plane of Eleven Antenna for 1 – 13 GHz

## Slide 19: Measured reflection coefficient of Eleven Antenna for 2 – 13 GHz

## Slide 20: Small Antennas – Part 2
Yagi antennas
Log-periodic wideband antennas
Microstrip patch antennas
Inverted F-antennas
Planar Inverted F-antennas
Miniaturization

## Slide 21: Microstrip Antennas
Microstrip antennas:
  etched metal patterns like strips, patches and slots.
Advantages:
  cheap to manufacture;
  mass produce;
  easy to use in linear, planar or conformal arrays;
  acurate design by numerical tool.
Disadvantages:
  used to be narrow band. But now can be wide band by aperture coupled;
  losses in substrate.

## Slide 22: Excitation methods

## Slide 23: About patch shapes
Patch shapes can be:
rectangular
circular
with slot
parasite strips
truncated corners
tuning stubs

## Slide 24: About polarizations
Linear polarization:
Symmetric patch
and excitation
Circular polarization: asymmetric patch
or excitation
Dual polarization:
Two feed lines or probes

## Slide 25: About polarizations
broadband circular polarization :
four patches in quadratic
sub-array with sequential 90 deg phase
Multi-band, broadband:
Stacked patches

## Slide 26: Microstrip line: Planar-waveguide model
Line:
Model:

## Slide 27: Microstrip line: Planar-waveguide model parameters
Empirical formulas:

## Slide 28: Microstrip line: Planar-waveguide model parameters

## Slide 29: Patch antennas: Analysis methods
Transmission line model (planar-waveguide)
Cavity method
Moment Method for patch current

## Slide 30: Rectangular patch: Transmission line model
quasi TEM wave with
b
e
eff
k
=
effective permittivity:
equivalent resonant length:
E-field under patch:
E
E
0
e
j
b
y'
–
z
ˆ
E
0
e
j
b
l
e
q
–
e
j
b
y'
l
e
q
–
(
)
z
ˆ
+
=
ff

## Slide 31: Rectangular patch: Dual slot model for radiation field function Thin substrate

## Slide 32: Rectangular patch: Dual slot model for radiation field function
G
r
ˆ
(
)
C
k
x
ˆ
r
ˆ
´
(
)
I
M
1
e
j
k
l
e
q
y
ˆ
r
ˆ
×
+
[
]
=
I
M
4
E
0
h
e
j
k
x'
x
ˆ
r
ˆ
×
(
)
x'
d
-weff
2
¤
–
weff
2
¤
ò
=
Strong radiation along the ground plane in E-plane

## Slide 33: Rectangular patch: E-plane radiation pattern (thin substrate)

## Slide 34: Rectangular patch: H-plane radiation pattern ?

## Slide 35: Impedance and resonant length of Rectangular line-fed patch

## Slide 36: Equivalent circuit for rectangular line-fed patch

## Slide 37: Rectangular patch: Resonant length and radiation resistance

## Slide 38: Rectangular patch: Input impedance by trans. line model

## Slide 39: Impedance of single patch antenna

## Slide 40: Small Antennas – Part 2
Yagi antennas
Log-periodic wideband antennas
Microstrip patch antennas
Inverted F-antennas
Planar Inverted F-antennas
Miniaturization

## Slide 41: Inverted F Antenna: IFA
A variant of the monopole + a loop in order to reduce the height.
The parallel section introduces capacitance to the input impedance of the antenna, which is compensated by the loop.
monopole
loop

## Slide 42: Inverted F Antenna: IFA
Ground plane:
  significant role in its operation.
  In general, roughly one quarter wavelength (λ/4) long.
The optimum location for omni-directional pattern and 50Ω impedance matching is close to the edge of the ground.
The polarization of the antenna is approximately linear but more accurately elliptical since the axial ratio rarely reaches 20 dB.

## Slide 43: Planar Inverted F Antenna: PIFA
Can be considered as a kind of Inverted F antenna (IFA) with the wire replaced by a plate.

## Slide 44: Advantages of PIFA
Can be hiding into the housing of the mobile when comparable to whip/rod/helix antennas.
Reduced backward radiation toward the user’s head, minimizing the electromagnetic wave power absorption (SAR) and enhance antenna performance.
Moderate to high gain in both vertical and horizontal polarization.

## Slide 45: PIFA : Quarterwave Patch Antenna

## Slide 46
PEC patch
substrate
infinite ground plane
infinite ground plane
feeding
feeding
y
PEC patch
substrate
microstrip patch
model of PIFA

## Slide 47: Increase the Bandwidth for PIFA
Adjusting the size of the ground plane.
Inserting several slits at the ground plane edges.
Use of thick substrate to lower the Q.
Using parasitic resonators with resonant lengths close to main resonant frequency.
Adjusting the location and the spacing between two shorting posts.
Excitation of multiple modes designed to be close together or far apart depending on requirements
Using Stacked elements.

## Slide 48: Dimensions of PIFA
The capacitive loading reduces the resonance length from l/4 to less than l/8 .The capacitive load can be produced by adding a plate (parallel to the ground) to produce a parallel plate capacitor.
The resonant frequency of PIFA can be approximate with:
L1 + L2 = λ/4
when W/L1=1 then L1 + H = λ /4
when W=0 then L1 + L2 + H = λ /4

## Slide 49: The effect of ground plane
IFA
PIFA

## Slide 50: Small Antennas – Part 2
Yagi antennas
Log-periodic wideband antennas
Microstrip patch antennas
Inverted F-antennas
Planar Inverted F-antennas
Miniaturization

## Slide 51: Miniaturization of antennas
Miniaturization by using
  Insert several slits
  Bending the structure
  Parasitic resonators
  ...

## Slide 52: Examples of Miniaturization of antennas: Planar Monopole

## Slide 53: Radiation pattern

## Slide 54: Examples of Miniaturization of antennas: Planar Monopole II

## Slide 55: Learning Goals
Describe the function of the elements in a Yagi antenna
Explain the design philosophy of a log-periodic antenna
Describe the main difference between a normal log-periodic antenna and the log-periodic eleven antenna
Explain how to feed a rectangular patch antenna for linear, dual and circular polarizations
Describe the dual slot model for the radiation field function for a rectangular patch antenna on a thin substrate
Apply design curves and formulas for the design of rectangular patch antennas

## Slide 56: Next lecture – May 12
Aperture antennas
  Aperture theory, aperture distribution…
  Fundamental gain limitations of large antennas
  Horn antennas
    Pyramidal, conical, corrugated