## Slide 1: Antenna Course 21-May-2015 Lecture 12
Dr. Andrés Alayón Glazunov

## Slide 2: From previous lecture: How to control the shape of the array beam?
There are five basic methods to control the overall antenna pattern:
the geometrical configuration of the overall array (linear, planar, conformal, etc.),
the relative placement of the elements,
the excitation amplitude of the individual elements,
the excitation phase of each element,
the individual pattern of each element

## Slide 3: Radiation field function of the array antenna
is the radiation field function of an element
AF is the array factor and can be expressed as
an element-by-element sum:
or as a grating lobes sum:
Radiation field function of the array:
The infinite sum converges fast for large arrays (often only the dominant p=0 and p=1 need to be included)

## Slide 4: Linear array: Some basic Principles
The neccesary condition for avoiding grating lobes is da<λ.
The sufficient condition for avoiding grating lobes is da<λ/2.
The element spacing da should be
to avoid grating lobes for certain maximum beam direction α0 .

## Slide 5: Lecture 11: Linear Array Antennas
Impedance of one element in an array
  Scan impedance
  Scan blindness

## Slide 6: Now we will analyze the impedance of one element in an array

## Slide 7: Example: 2 dipole array
Reciprocity gives
Self-impedance of dipole 1:

## Slide 8: Example: 2 dipole array
Reciprocity gives
Self-impedance of dipole 2:

## Slide 9: Mutual impedance between two dipoles
Mutual impedance between dipole 1 and dipole 2:

## Slide 10: Mutual impedance between two dipoles
Mutual impedance between dipole 2 and dipole 1:

## Slide 11: From the reciprocity:
Mutual impedance between two dipoles
=

## Slide 12
=
=
=
Mutual impedance between two dipoles
Reaction integrals
Reciprocity

## Slide 13: Plot of mutual impedances between two halfwave dipoles:

## Slide 14: Scan Impedance

## Slide 15: Linear array: Equivalent circuit
Total voltage at terminal of dipole m

## Slide 16: Linear array: Scan impedance
When phase steering the array, we supply the voltages (excitations)
Current on element m must be solved from these N equations:
Scan impedance of each element m is then found to be:

## Slide 17: Linear array: Scan impedance
If Am = A and ΔΦm=ΔΦ , scan impedance is almost the same for all elements except for edge elements
The scan impedance varies with scan angle α0

## Slide 18: Quiz
Is the scan impedance equal to the embedded element impedance or is it equal to the isolated element impedance ?
The answer is No, in both cases.
The embedded element impedance is determined when the other array elements are in place and match terminated, the scan impedance is determined when the other array elements are in place and excited, and the isolated element impedance is determined when the other elements are not present.

## Slide 19: Scan blindness
The scan impedance changes with the direction α0 of the main lobe.
If we match the scan impedance to the source (or transmission line) impedance at broadside (α0 = 90), we will get mismatch and corresponding power loss when the beam is scanned away from broadside.
At some angle the scan impedance changes very rapidly
  Leads to big impedance mismatch.

## Slide 20: The Reasons for Scan blindness
Sudden appearance of a grating lobe in the visible region
  element pattern is broad and
  The grating lobe is in the direction of the array. Therefore, very strong mutual couplings among elements
structure can support surface waves and wavenumber of surface wave satisfies
  which also leads to strong mutual couplings among elements

## Slide 21: The Reasons for Scan blindness
a) Grating lobe
b) Support surface waves
-ksw/k
ksw/k
Delta function representing surface wave as part of element pattern

## Slide 22: Lecture 12 Array Antennas – Planar Array
Planar array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Shape and width of main lobe for planar array
Condition for non-radiating grating lobes
Directivity and Sub-efficiencies
  Grating lobe efficiency
  Illumination efficiency
  Polarization efficiency

## Slide 23: Learning goals of the Lecture
Explain the analysis of planar phased array
  Array factor as element-by-element sum
  Array factor as grating-lobe sum.
Describe the shape and width of main lobe for planar array
Describe the condition for non-radiating grating lobes
Calculate Directivity, sidelobes and grating lobes

## Slide 24: Lecture 12 Array Antennas – Planar Array
Planar array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Shape and width of main lobe for planar array
Condition for non-radiating grating lobes
Directivity and Sub-efficiencies
  Grating lobe efficiency
  Illumination efficiency
  Polarization efficiency

## Slide 25: Planar Arrays
Consist of elements located
in a planar 2D grid
an array of linear arrays
rectangular grid
triangular grid
Different types of grids:
Design goal:

## Slide 26
Planar Array of Equispaced Elements
Elements are located with their phase reference points at
for m=1,2,…,M
and n=1,2,…,N
rectangular aperture
rectangular grid

## Slide 27: Planar array: Array factor as element-by-element sum
Array factor
Embedded radiation function
of element

## Slide 28
  Array factor as element-by-element sum is convenient only for small arrays
  Array factor as infinite grating lobe sum

## Slide 29: Planar array: Definition of the excitation distribution
is the amplitude excitation function

## Slide 30: Planar array: Definition of the excitation distribution
Propagation constants of the phase excitation:
Smooth and continuous phase excitation function:

## Slide 31: Planar array: AF as a grating-lobe sum
Double Fourier transform of the excitation distribution:
Array factor is sum of equal contributions
Each one is centered around its maximum for which:
and

## Slide 32: For a graphical representation of AF
will be represented as a function of
For a linear array
{o, o}

## Slide 33: Graphical representation of an element pattern
For a linear array
The element pattern, represented as a function of
and

## Slide 34: Planar array: Graphical representation of AF
A(x,y) = 1 and ΔΦx = ΔΦy = 0
Main lobe of AF will be narrower than the element pattern
Grating lobes will have the same shapes, and will be displaced w.r.t each other
Main lobe direction  the 1st maximum of AF (coincides with Z axis)
{o =0, o=0}
Circular aperture.
Rectangular grid.

## Slide 35: Planar array: Graphical representation of AF
A(x,y) = 1 and ΔΦx = ΔΦy = Const
{o, o}

## Slide 36: Planar array: Graphical representation of the total array radiation pattern contours
{o, o}
A(x,y) = 1 and ΔΦx = ΔΦy = Const

## Slide 37: Planar array: Graphical representation of AF with main lobe and grating lobes. Circular aperture. Rectangular grid.
A(a) = 1 and ΔΦ = Const
{o, o}

## Slide 38: 3 dB beamwith
Aperture Antennas
Array Antennas
aperture
aperture
beam
b
b
beam
Array
Array
beam
b
b
beam

## Slide 39: Planar array: Direction of the main lobe
First maximum of array factor when p=q=0:
corresponding to:
i.e.

## Slide 40: Lecture 12 Array Antennas – Planar Array
Planar array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Shape and width of main lobe for planar array
Condition for non-radiating grating lobes
Directivity and Sub-efficiencies
  Grating lobe efficiency
  Illumination efficiency
  Polarization efficiency

## Slide 41: Planar array: shape and width of main lobe
Shape of main beam is determined by
Beam width k(φ) – is independent of the values of and
Beam width (φ) – does dependent of the direction of the main lobe
{o, o}
translation
{o =0, o=0}
{o , o}
{o,  o}
Z
X
Y
 o=0
 o=90
projection

## Slide 42: Planar array: Shape and width of main lobe
{o =0, o=0}
{o , o = 0}
{o,  o= pi/2}
X
Y
 o=0
 o=90
 o=0
Z
Beam width (φ), corresponding to beam width k(φ):
[rad]
When the scan angle o increases:
Beam width (φ) broadens as 1/cos(q0) in plane of scan φ0
Beam width (φ) remains the same in plane of scan φ =φ0+90o

## Slide 43: Planar array: Shape and width of main lobe
We see that the beamwidth broaden as
1/cos 0 in the plane of scan 0 when the scan angle 0 increases.
There is no beam broadening in the plane orthogonal to the scan plane.

## Slide 44: Why is the beam width (φ) a factor 1/cos(θ0) larger in the scan plane?
0
-ΔΦ
-2ΔΦ
-3ΔΦ
-4ΔΦ
L
α
Lcosα
Projection of the aperture into the scan direction

## Slide 45: Lecture 12 Array Antennas – Planar Array
Planar array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Shape and width of main lobe for planar array
Condition for non-radiating grating lobes
Directivity and Sub-efficiencies
  Grating lobe efficiency
  Illumination efficiency
  Polarization efficiency

## Slide 46: Planar arrays: Direction of grating lobes
Grating lobe maxima when
Corresponding to
Rectangular grid of grating lobes in spectral domain. Shape determined by

## Slide 47: Planar array: Condition for non-radiating grating lobes
No visible grating lobes when
The grating lobes can also be suppressed by the element pattern.

## Slide 48: Illustration of the main lobe and its width in different planes for the case in slides 32-35

## Slide 49: The Sufficient and Necessary Condition for non-radiating grating lobes
The four red grating lobes are out of the visible region at the SAME time

## Slide 50: Sufficient Condition for non-radiating grating lobes
The sufficient condition is in a simple form as

## Slide 51: Sufficient Condition for non-radiating grating lobes
If we steer the beam from –π to π for φ0, we have sufficient condition for non grating lobes as

## Slide 52: Grating lobe mittigation

## Slide 53: Lecture 12 Array Antennas – Planar Array
Planar array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Shape and width of main lobe for planar array
Condition for non-radiating grating lobes
Directivity and Sub-efficiencies
  Grating lobe efficiency
  Illumination efficiency
  Polarization efficiency

## Slide 54: Planar array: Directivity
Maximum available directivity
Grating lobe, polarization, aperture illumination efficiency
Aperture projection factor

## Slide 55: Subefficiencies: illumination efficiency
Aperture illumination efficiency:

## Slide 56: Sub-efficiencies: Polarization Efficiency
Polarization efficiency:

## Slide 57: Subefficiencies: Grating lobe efficiency
Grating lobe efficiency:
The grating lobe efficiency is independent of the shape of the aperture,
i.e. of the contour of A (x,y), i.e. whether this is circular, quadratic or rectangular.

## Slide 58: Comparison between Linear and Planar array: directivity and grating efficiencies
Linear
Planar

## Slide 59: Why we have cosθ0 in Planar array but not in Linear array for directivity
Linear
Planar
Aeffective=cosθ0A
Effective area
Even the beam width is broaden,
the directivity is kept the same when the beam is steered because the volume of the kind of “ring cone” is the same with the same directivity and broaden beamwitdh (volume means power)
Same volume

## Slide 60: Aperture antennas versus Array antennas
Never have grating lobes
Dmax=4π/λ2·A
3 dB beamwith
First sidelobe
  -13.2dB
  -17.6dB
Risk to have grating lobes
Dmax 4π/λ2·A if no grating lobe
3 dB beamwith
First sidelobe
  -13.2dB
  -17.6dB
Aperture Antennas
Array Antennas

## Slide 61: Quiz 2
Open waveguide array as shown in figure.
Do we have grating lobes in E- and H-planes if we excite the array uniform in amplitude and in same phase? Assume that we have TE10 mode in the waveguide.
E
λ
λ

## Slide 62: Quiz 2
We do not have grating lobes in E-plane if we excite the array uniform in amplitude and in same phase?
  We can get this conclusion by two ways.
    Since the aperture distribution of the TE10 mode is uniform in E-plane, the whole array aperture distribution is continuous uniform. Therefore, we can consider the array as a continuous uniform aperture antenna so there is no grating lobes (only discrete arrays have grating lobes).
    Using array theory, since the element spacing is λ, the grating lobe is just coming into the visible region at 90 deg from the broadside for array factor. But the radiation function of the element waveguide is zero at 90 deg, which you can get from figure 7.12. Therefore, the total radiation function of the array is the radiation function of the element waveguide multiplied by array factor, no grating lobe at 90 degree.
Do we have grating lobes in H-planes if we excite the array uniform in amplitude and in same phase?
  Yes.