## Slide 1: Antenna Course 23-Apr-2015 Lecture 6
Dr. Andrés Alayón Glazunov

## Slide 2: Lecture 6 Characterization of antennas in multipath
  MIMO and MIMO characterization
  Measurements in reverberation chamber
    Characterization of active terminals: TRP, TIS, Throughput data rate
  System Modelling
    Threshold Receiver: Probability of Detection (PoD), throughput

## Slide 3: Learning goals (after lab 1)
Describe how reverberation chambers work.
Describe how reverberation chambers can be used to measure MIMO antenna performance in rich isotropic multipath
Describe how reverberation chamber can be used to measure active terminals: Calibration of chamber and measurements

## Slide 4: Lecture 6 Characterization of antennas in multipath
  MIMO and MIMO characterization
  Measurements in reverberation chamber
    Characterization of active terminals: TRP, TIS, Throughput data rate
  System Modelling
    Threshold Receiver: Probability of Detection (PoD), throughput

## Slide 5: What is MIMO?
MIMO = Multiple Input Multiple Output
Multiple transmit (Tx) antennas & Multiple receive (Rx) antennas are used to produce multiple data streams
4G and Beyond (e.g., 5G) Communications Systems

## Slide 6: MIMO system in multipath environment, Shannon’s extended formula (CSI = Channel state information)
No CSI at transmitter, full CSI at receiver, power equally divided:
H is the channel matrix containing all S-parameters between all Tx and all Rx ports
nt = 1, 2, …M antenna ports
nr = 1, 2, …N antenna ports
Rich scattering environment causing Rayleigh fading
Tx ports
Rx ports

## Slide 7: Result measuring the channel measurements and using channel capacity formula for 3x6 MIMO. Effect of mutual coupling/correlation.
3x6 MIMO
Reduction in capacity for small element spacing d is due to reduction in embedded element efficiency of each monopole, and correlation between channels
d
d =

## Slide 8: MIMO capacity for SNR = 15 dB antenna modeled in IE3D and and external RIMP ray model. Measurements in reverberation chamber.

## Slide 9: MIMO concepts in modern digital communication systems
MIMO (and communications in general) requires an estimate (measurement) of the channel matrix H.
For small SNR in rich isotropic multipath:
  Antenna diversity by Maximum Ratio Combination (i.e. superposition by complex conjugate channel weighting)
For large SNR
  MIMO multiplexing/multi-stream may produce two or more bit streams at same frequency to drastically multiply channel capacity
  Processing involves diagonalization of the channel matrix (eigenvector formation). Each eigenvector represents a “bit stream channel” (channel must be known at both the receiver and the transmitter).
For large SNR in LOS environments:
  MIMO reduces to classical beam-forming, 2 beams (bit streams) can be formed when using 2x2 MIMO if the ports excite orthogonal polarizations.
  We can also achieve 2 bit streams by using co-polar elements with large separation (not practical).
For large SNR in advanced systems
  MultiUser MIMO, i.e. many send different bit streams at same frequency to different users in same environment, Massive MIMO.

## Slide 10: Lecture 6 Characterization of antennas in multipath
  MIMO and MIMO characterization
  Measurements in reverberation chamber
    Characterization of active terminals: TRP, TIS, Throughput data rate
  System Modelling
    Threshold Receiver: Probability of Detection (PoD), throughput

## Slide 11: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 12: Friis transmission formula between two antennas in free space (LOS)
Power density:
Received power:
Friis transmission equation:
(free space Attenuation or Pathloss)

## Slide 13: Friis transmission formula between two antennas in free space (LOS)
Power density:
Received power:
Friis transmission equation:
(free space
attenuation)
This lecture is about multipath, NOT LOS

## Slide 14: Learning goals
Describe how antennas in multipath environment with fading behave and are characterized
Explain the different factors contributing to the antenna efficiency and diversity gain in multipath

## Slide 15: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 16: Transmission between two antennas in multipath environment
Power density:
Received power:
Friis transmission equation:
(free space attenuation or pathloss)

## Slide 17: Multipath environment
Many different propagation paths are summed up at a receiving antenna. The sum is described by the Rayleigh probability distribution. FADING!
Transmitter
Receiver

## Slide 18: Definition of the channel
The channel is defined as the transfer function (e.g. S21) between the port of the transmitting antenna and the port of the receiving antenna.
Thus, both the transmitting and receiving antennas are included in the channel.

## Slide 19: The wireless channel
For the successful deployment of wireless communications systems in terms of capacity and coverage it is necessary to suppress or even take advantage of the wireless channel impairments:
  Fast fading (short-term fading)
  Shadowing (long-term fading)
  Pathloss
  and
  Interference and/or noise!
Multipath propagation is the main
propagation mechanism in wireless
communications systems
  Fast fading is a result of local scattering
  Shadowing is due to scattering by large objects
The antennas or rather their interactions with the channel are also contributing factors to the radio propagation channel

## Slide 20: Received voltage fades when moving around in multipath environment

## Slide 21: Statistical representation of voltage: Rayleigh distribution
CDF = Cumulative Distribution Function

## Slide 22: Questions
What is the statistical distribution of the complex received voltage?
What is the CDF of the received power?
What is the CDF with the LOS component called?

## Slide 23: Central limit theorem applied to multipath
Many independent complex values (i.e., both amplitude and phase)
Complex Gaussian Probability Distribution
Then, the envelope (i.e., the absolute value) of the received voltage has a Rayleigh distribution
The received power has an Exponential distribution

## Slide 24: Cumulative probability distribution of fading
Complex Gaussian random variables
Abs(V)
Re(V)
Im(V)
Rayleigh CDF if voltage is depicted and Exponential CDF if power is depicted

## Slide 25: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 26: Equivalent circuits – Still valid
Transmitting antenna

## Slide 27: Equivalent circuits – Still valid
Receiving antenna
Same as for LOS
but summed over many
incident waves

## Slide 28: Angles of Arrival (AoA)
The Angles of Arrival are the angles k and k for which Ek 0 (or large enough)
In practice the K largest contributions, i.e., impinging waves, are taken into account.

## Slide 29: Cross-polar Power Discrimination (XPD)
The incident field can be represented as the sum of a vertically polarized (VP) component and a horizontally polarized (HP) component, i.e., Ek =Ek, VP + Ek, HP
Real environments normally have a larger content of vertically polarized wave component than horizontal, because most base stations are vertically polarized.
This is in propagation literature characterized by a Cross-polar Power Discrimination (XPD) or Cross-Polarization Ratio (XPR)
In this course we call this ratio the polarization imbalance

## Slide 30: Question
What happened with the factor
(1/r)exp(-jkr)
in this formula for received voltage:

## Slide 31: Rich Isotropic MultiPath environment – (RIMP) Reference environment
The RIMP environment is characterized by
polarization balance of the impinging waves, i.e., XPD=1 (or 0 dB) and
uniform distribution of the Angles of Arrival (AoA) of the impinging waves, over the unit sphere.

## Slide 32: Computer emulation of isotropic multipath environment
Define a set of K incident waves
Each wave should have:
Complex Gaussian distribution (i.e. both real and
imaginary parts normal (Gaussian) distributed)
Uniformly distributed AoA over the unit sphere
(i.e. phi uniformly and theta sinusoidal weighted distr.)
Uniformly distributed polarization angle
Compute the port voltage due to the K waves
Repeat for a
“sufficient”
number of
scenarios

## Slide 33: Illustration of isotropic environment 20 waves (one realization), Ez-field plot
Each square is a part of a wavefront.
Black line is E-field direction and amplitude.
Radial location is phase.
Central color plot shows spatial variation of Rayleigh distributed Ez field.

## Slide 34: Simulated received power in isotropic environment (compared to maximum available). 20 waves/realization. 3 different antenna orientations.
Relative received power (dB)

## Slide 35: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG : Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 36: Far-Field Function and antenna impedance
An antenna is characterized by the far-field function G(,) and the antenna impedance Za.
In RIMP the actual directions of radiations are not relevant for single-port antennas!
To quantify the voltage (or power) transfer to/from the antenna port from a transmitter/receiver through a transmission line with characteristic impedance Zc we define the reflection coefficient

## Slide 37: Definition of MEG (Mean Effective Gain)
MEG is the average received power relative to an antenna which receives two orthogonal polarizations from all directions.
What is then the reason for MEG=-3 dB and not 0 dB of an ideal antenna in isotropic environment?
Relative received power (dB)
We need two orthogonal ports to receive two polarizations.

## Slide 38: Characterization of received power on a single-port antenna
Line of Sight (LOS) system:
  Realized gain = Directivity X Radiation efficiency
Multipath or rich scattering environment:
    MEG = MED X Radiation efficiency
  MEG (MED) = Mean Effective Gain (Directivity) is a weighted average of the radiation intensity.
  The weights are the elevation and azimuth power-angle distributions of the impinging waves.
  MEG = Radiation efficiency/2 in isotropic environment

## Slide 39: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 40: Total radiation efficiency characterizes performance in rich isotropic multipath
Total radiation efficiency = Radiated power / Max available power
Total radiation efficiency has 3 contributions:
  Mismatch factor: Reflections on input port
  Radiation efficiency:
    Absorption in antenna materials
    Absorption in lossy object such as head phantom

## Slide 41: Power expressions for single-port antenna

## Slide 42: Efficiencies for single-port antenna

## Slide 43: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
  How to model an antenna in a multipath channel
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 44: Moving around in multipath environment causes fading of received voltage

## Slide 45: Illustration of isotropic environment 20 waves (one realization), Ez-field plot
Each square is a part of a wavefront.
Black line is E-field direction and amplitude.
Radial location is phase.
Central color plot shows spatial variation of Rayleigh distributed Ez field.

## Slide 46: Two separated antennas for diversity
Transmitter
Antenna
branch 1
Antenna
branch 2
Multipath
environment

## Slide 47: Two independent fading channels

## Slide 48: Selection combining of the two channels
Choose the strongest
antenna branch!
This avoids deep
fading dips.
Combined signal has also
higher SNR.

## Slide 49: Diversity gain by selection combining normally given at 1 % CDF
Normalized power (dB)

## Slide 50: Diversity and combining methods
Antenna diversity:
  Polarization diversity
  Space diversity
  Pattern diversity
The idea is to exploit received signals with low correlation (i.e., fading dips do not occur simultaneously)
Combining techniques
  Selection-combining (SC)
  Maximal-Ratio-combining (MRC)
  Equal-gain-combining (EGC)
  …
  …

## Slide 51: Diversity Characterization
We need to know the signal processing algorithm.
Let’s look at the MRC algorithm of a multi-port antenna diversity system.
The signals received at the antennas form a linear combination
where the optimal weights in the sense of maximizing SNR are chosen as the complex-conjugate of the estimated channels at each antenna, i.e.,

## Slide 52: Example: Application of MRC
Slot antennas on an infinite ground plane
Each slot can be approximated by an elementary magnetic dipole source with omnidirectional pattern on the xz-plane
The co-polar far-field function of each element i on the xz-plane is then given by
We consider only isolated elements

## Slide 53: Example: Estimated Channel
Let’s assume that we have Q incident waves from directions q with equal amplitudes but different phases q
Then the total induced voltage at antenna element i is given by

## Slide 54: Example: MRC signal
The received combined signal becomes then, by using the complex-conjugate weights
The far-field function for the whole antenna is obtained by summing up all far-field functions over all elements by using the estimated channel weights as port weights.

## Slide 55: Far-Field Patterns of the MRC Algorithm
1 wave (like in LOS) arriving at 0 or 60 degrees
2 waves
4 waves

## Slide 56: Conclusion on Far-Field Patterns of the MRC Algorithm
We will not be able to form directive beams towards the AoAs unless there are more antenna ports than waves in the environment.
The MRC algorithm is still generally referred to as beam-forming, and it is the optimum way of combining the channels to achieve the highest signal-to-noise ratio.
For larger arrays the conclusion will be the same.

## Slide 57: Diversity Gains
The diversity gain is the difference in dB between the MRC CDF and a reference Rayleigh CDF at a certain CDF-level, normally chosen to be 1%.
We can distinguish between apparent, effective and actual diversity gains depending on what kind of reference we use.
The reference is a Rayleigh-shaped CDF corresponding to an ideal antenna with 100% efficiency, and therefore the dB value is referred to as a dBR value.

## Slide 58: Diversity Gains
Apparent diversity gain: The reference CDF is the CDF at the port with the strongest average power levels.
Effective diversity gain: The reference CDF is the CDF at the port of the ideal reference antenna, i.e., the theoretical Rayleigh CDF.
Actual diversity gain: The reference CDF is the CDF at the port of an existing practical single-port antenna. The latter is then normally the single-port antenna that is to be replaced by the diversity antenna under test, so that we can determine the actual improvement over an existing solution. Both antennas must therefore be measured at the same location, e.g., relative to a head phantom.

## Slide 59: Diversity Gains
?
CDF of the ideal reference antenna (corrected for its finite radiation efficiency) and of a diversity antenna consisting of two parallel dipoles separated by 0:05.

## Slide 60: What limits the diversity gain?
Theoretical limits
Embedded element efficiency
Correlation (i.e. how equal the two antenna elements are, the more different the better in amplitude, phase and polarization)

## Slide 61: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 62: Power expressions for a 2-port (lossless) antenna (characterize easiest on transmit)
Pavail is the available power active port 1 from matched source.
Prefl,1=Pavail|S11|2 is the reflected power from port 1.
Pabs,2=Pavail|S21|2 is the power absorbed by the match-terminated port 2.
Pacc,1=Pavail - Prefl,1 is the accepted power by port 1.
Prad,1=Pacc,1 - Pabs,2 since the antenna is lossless.

## Slide 63: Efficiencies for (lossless) multi-port antennas
erefl,1=Pacc,1/ Pavail is the matching efficiency on port 1
eabs,1=Prad,1/ Pacc,1 is the radiation efficiency of port 1
erad,1=Prad,1/ Pavail = erefl,1eabs,1 is the total (embedded) efficiency of port 1
And expressed as functions of the S-parameters
erefl,1=1-|S11|2
eabs,1=(1-|S11|2 -|S21|2)/ (1-|S11|2)
erad,1= 1-|S11|2 -|S21|2 is the total (embedded) efficiency of port 1

## Slide 64: Efficiencies for 2-port antennas, 2-dipole antennas

## Slide 65: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 66: Embedded element far-field function
…is defined as
  The far-field function for each single antenna element when all other elements are present and terminated (normally in 50 ohm)

## Slide 67: Embedded element far-field function
Isolated far-field function
for dipole
Embedded element far-field function
for dipole 1, i.e. when dipole 1 is
excited and dipole 2 is terminated
Embedded element far-field function
for dipole 2, i.e. when dipole 2 is
excited and dipole 1 is terminated

## Slide 68: Lecture 5 Characterization of antennas in multipath
Multipath environment and Rayleigh fading
How to model the multipath channel?
Single-port antenna characterization in multipath
  MEG – Mean Effective Gain
  Efficiencies
Multi-port antennas characterization in multipath
  Diversity gain
  Efficiencies
  Embedded element far field function
  Mutual coupling
  Correlation

## Slide 69
Example: Two parallel dipoles, mutual coupling Equivalent circuit of one embedded element
50
Zin
Input impedance
I1
Zd1

+
-
I2
RL
Transmission line
l
Zc=50
Z12I1
+
-
Distance
between
dipoles
d
Zd2
Z12I2
+
-
V1
Mutual impedance Z12
Reflection coefficient 
at antenna port 1
Antenna 1
Antenna 2
Mutual coupling may cause decorrelation (more different element patterns)
and large reduction in radiation efficiency.
Separation between dipoles
d
Receiver and/or transmitter of port 1
Diversity combination (RX) and/or separation (TX)
Receiver and/or transmitter of port 2

## Slide 70: Efficiencies for (lossless) multi-port antennas
erefl,1=Pacc,1/ Pavail is the matching efficiency on port 1
eabs,1=Prad,1/ Pacc,1 is the radiation efficiency of port 1
erad,1=Prad,1/ Pavail = erefl,1eabs,1 is the total (embedded) efficiency of port 1
And expressed as functions of the S-parameters
erefl,1=1-|S11|2
eabs,1=(1-|S11|2 -|S21|2)/ (1-|S11|2)
erad,1= 1-|S11|2 -|S21|2 is the total (embedded) efficiency of port 1

## Slide 71: Three ways to determine the complex correlation coefficient between port voltages in RIMP
From embedded element far-field functions
From S-parameters of the antenna (for lossless antennas only)
From measured port voltages (channels)

## Slide 72: Diversity Characterization
Correlation between the ports of two parallel half-wave dipoles in RIMP (left), and the apparent and effective diversity gains by MRC versus dipole spacing(right).

## Slide 73: Next lecture – April 23
Characterization of antennas in multipath
  MIMO
  Characterization of active terminals
    TRP, TIS, throughput
  Threshold receiver model
  Measurements in reverberation chamber

## Slide 74: Learning goals
Describe how antennas in rich isotropic multipath are characterized.
Explain the different factors contributing to the antenna efficiency and diversity gain in multipath