## Slide 1: 1. Introduction
Applications
Antenna types and classes
Brief history of antennas and analysis methods
Terminology and units
Vector notation

## Slide 2: Learning goals
Describe
  where antennas are used
  some antenna types and beams
  terms such as radiation, scattering, rays, phase fronts, reflection, diffraction
Explain
  how dB values are related to physical quantities measured in A, V or W

## Slide 3: What is an antenna?
Device for transmitting or receiving electromagnetic waves
Transducer between free space and transmission line
Directional spatial filter
Some other old words for antenna
  Aerial
  Radiator

## Slide 4: Some notes about electromagnetic (EM) field
EM field is a vector
  3 components in 3 dimensional space
  polarization
EM field changes with time
  Time-harmonic EM field is a complex value
EM field changes with location
  A function of location in 3D space, need some imaging of space

## Slide 5: Antenna Applications
Ground based telecommunication systems:
    direct broadcasting
    radio links
    mobile phones and base stations
    Other wireless devices
    traffic toll
    navigation
Satellite communication systems:
    linking ground based systems at long distance
    satellite-TV
    mobile earth terminals/ mobile phones

## Slide 6: Antenna Applications
Civilian and military radar:
    weather radar
    air traffic radar
    military search and scouting radar
    synthetic aperture surveillance radar (SAR) (pollution, traffic, fishing borders)
    Ionospheric and planetary research
Radiometers:
    military early warning system
    radio astronomy & SETI
    meteorology & land resources surveillance

## Slide 7: Antenna Technologies
The antenna is often the largest and most expensive part of a microwave system
  System technology
  Field theory
  Antenna theory and analysis methods
  Programming and CAD simulations
  Materials technology (also artificial materials, also called metamaterials)
  Manufacturing techniques
  Experimental development
  Measurements
Traditional antennas were used for Line-Of-Sight (LOS)
Modern antennas are often used in multipath with Rayleigh fading, without LOS.
Since 2008:
  New lecture about characterization of small antennas in multipath
  Lecture about fundamental limitations of antennas

## Slide 8: Antenna types
Wire Antennas
Slot Antennas
Microstrip Antennas
Horn Antennas
Reflector Antennas
Dielectric Resonator Antennas
Leaky Wave Antennas

## Slide 9: Examples of different antenna types

## Slide 10: Different phased array antennas
Today this is called a
MIMO array

## Slide 11: Array antenna types
Linear and Planar Array Antennas:
Phase-steered Array Antennas
Active Arrays
MIMO arrays
  Signal Processing Antennas
  Digital Beam Forming
  Adaptive Antennas

## Slide 12: Classes of Antenna Beams

## Slide 13: Quiz 1
What kind of beam does your mobile phone antenna have?

## Slide 14: Terminology and units
Radiation or scattering
Reflection, refraction, edge diffraction, aperture diffraction
Rays, waves, phase fronts, phase paths
Field and source units and dB

## Slide 15: Radiation / scattering

## Slide 16: Reflection, refraction, edge diffraction, aperture diffraction

## Slide 17: Rays, waves, phasefronts (or wavefronts), phase paths

## Slide 18: Units and dB
Electric field density E Volt/meter
Magnetic current density M Volt/meter
Magnetic field density H Ampere/meter
Electric current density J Ampere/meter

## Slide 19: Definition of dB
In Antenna Engineering, we use dB
  dB is a relative measure, i.e., always compared to a reference value
  dB is always a power ratio
  dB value is always between 0 and ±200, easy to communicate
A = amplitude of E-field density
P = power density of wave

## Slide 20: dBi and dBm
dBi means the reference is the isotropic antenna
dBm means the reference is 1 milliwatt.
dB/K means the reference is 1/K

## Slide 21: Amplitude and power ratios and their dB values
Amplitude ratio | 32 | 10 | 3.2 | 1 | 0.32 | 0.1 | 0.032 | 0.01
Power ratio | 1000 | 100 | 10 | 1 | 0.1 | 0.01 | 0.001 | 0.0001
Ratio in dB | 30 dB | 20 dB | 10 dB | 0 dB | -10 dB | -20 dB | -30 dB | -40 dB
Unit | dBi | dBm | dBW | dB/K
reference | isotropic | 1 mW | 1 W | 1/K
“Absolute” dB values

## Slide 22: Use dB, not %
Antenna efficiencies:
Good antenna engineers can control 0.1 dB
Measurement accuracy on gain, typ. 0.3 dB
Percent value | 100% | 99% | 95% | 90% | 80% | 64% | 50% | 25% | 10% | 5%
dB value | 0 dB | -0.04 dB | -0.22 dB | -0.5 dB | -1 dB | -2 dB | -3 dB | -6 dB | -10 dB | -13 dB

## Slide 23: Quiz 2
ǀS11ǀ=0.1, S11= ̵ 20 dB or ̵ 10 dB?

## Slide 24: Explanation of symbols

## Slide 25: The most used vector formulas:
Scalar (dot) product C=A•B

## Slide 26: The most used vector formulas:
Vector cross product c=a×b

## Slide 27: The most used vector formulas:
Removal of component of B in direction â to obtain C normal to â: C=B-(B•â) â
(B•â) â
B
â
C

## Slide 28: The most used vector formulas:
A dyad is a notation for a vector operation, e.g., D is a dyad if we write
B•D=B-(B•â) â

## Slide 29: The most used vector formulas:
Scalar (dot) product C=A•B
Vector (cross) product C=AxB
Removal of component of B in direction â to obtain C normal to â: C=B-(B•â) â
A dyad is a notation for a vector operation, e.g., D is a dyad if we write C=B•D=B-(B•â) â

## Slide 30: Brief History
Maxwell’s equations 1864
Hertz 1888: parabolic metal cylinder
Marconi 1901: Transatlantic transmission
World War II: Radiating apertures, reflectors, Arrays

## Slide 31: Brief History
Maxwell’s equations 1864
  One of the most beautiful equations

## Slide 32: Brief History
The first parabolic antenna, built by Heinrich Hertz in 1888

## Slide 33: Brief History
Marconi 1901: Transatlantic transmission
Marconi watching associates raising the kite used to lift the antenna at St. John's, Newfoundland, December 1901

## Slide 34: Brief History: Ray methods
    Euclid 300 BC: reflection law
    Alhazan 1000: lens Snell 1621: refraction
    Fermat, Hamilton 16-18 century: classical geometrical optics
    Sommerfeld 1884: edge diffraction
    Luneberg 1944, Kline 1951: modern geometrical optics (GO)
    Kouyoumjian, Pathak 1974-81: uniform geometrical theory of diffraction (UTD)
    Several more authors 1960-today: asymptotic techniques
  In this course: a bit GO

## Slide 35: Brief History, wave theories
    Huygen’s 1690: Huygen’s principle
    Fresnel 1830
    Maxwell 1864: Maxwell’s equations
    Schelkunoff 1936: Equivalence principle
  In this course: A lot of equivalence

## Slide 36: Brief History, numerical methods
Galerkin, 1871-1945: Galerkin’s method
Harrington, 1968: Moment Method (MM)
  Also known as Boundary Element Methods
Finite Element Methods (FEM)
Finite Difference Time Domain Method(FDTD)
Spectral domain techniques
  (spectrum of plane wave solutions)
  (spectrum of 2D field solutions)
In this course: Simple MM for deriving integral solutions

## Slide 37: Learning goals
After this lecture and additional reading you should be able to summarily describe
  where antennas are used
  some antenna types and beams
  terms such as radiation, scattering, rays, phase fronts, reflection, diffraction
and explain (repetition)
  how dB values are related to physical quantities measured in A, V or W