## Slide 1: Lecture 3 In this lecture, we are only dealing with antennas for Line-of-Sight systems (or in other words, in free space)
1. BOR Antenna 2. Antenna System Performance
Jian Yang
jian.yang@chalmers.se
Room 7312

## Slide 2: Learning goals of the Lecture
Describe the definitions of BOR antennas and the importance.
Describe the characteristics of BOR antennas.
Describe how to characterize antenna systems
Explain the different factors contributing to the efficiency and gain of different types of antennas, as well as to system noise temperature.
Notes: Describe - to tell or depict in written or spoken words, without using the textbook;
Explain - to make known in detail, including the simplest basic equations, without using the textbook

## Slide 3: Definition of BOR antennas
BOR (Bodies Of Revolution) antennas:
  completely rotationally symmetric geometry around one axis.
  Usually we align this axis on z-axis
    to make the analysis easier.
The far field of BOR antennas
  can have an azimuth (φ) variation.
  The order of this variation is characterized by an index on BOR.

## Slide 4: Definition of BOR antennas
In short, a BOR antenna is
  Geometry has no azimuth (φ) variation.
  The far field of BOR antenna can have an azimuth (φ) variation.
BORindex
geometry
Field variation

## Slide 5: Why do we concern about BOR antennas (the importance)
Many antennas are BOR antennas.
In reflector antennas, the parabolic reflectors are of BOR geometry.
Feeds for reflectors may not be of BOR geometry
  but only BOR1 component of the field contribute to the gain of the antenna.

## Slide 6: Examples of BOR antennas
Circular horn
Yes
Yes
No

## Slide 7: Examples of BOR antennas
Z
X
Y
Z
X
Y
X
dipole
Y-polarized dipole
Incremental electric current (dipole)
Z
Y
Yes
Yes
No

## Slide 8: Examples of BOR antennas
By definition, it is not BOR antenna.
Later on, you will see, the far field of this antenna is very close to that of BOR1 antenna.
So we (engineers) often call this antenna also as a BOR antenna.
Yes or No?
Short dipole

## Slide 9: BOR0 antennas
BOR = Geometry of Bodies of revolution
BOR0 antennas
  The far field has no azimuth (φ) variation:
BOR0
Field no φ variation

## Slide 10: BOR0 antenna Examples
Electric dipole on z-axis:
Z
X
Y
Far field function:

## Slide 11: BOR0 antenna Examples
Magnetic dipole on z-axis :
Z
X
Y
Z
X
Y
Far field function:
Magnetic dipole
loop

## Slide 12: BOR1 antennas
BOR = Geometry of Bodies of revolution
BOR1 antennas
  The far field has the first order of azimuth (φ) variation:
  sinφ or cosφ
BOR1
Field sinφ or cosφ function

## Slide 13: Examples of BOR1 antennas
Circular horn with y-polarized TE11 mode excitation in circular waveguide:
X
Y
Z
Notes: Draw TE11 field

## Slide 14: Examples of BOR1 antennas
Incremental electric current (dipole) with y-polarization (or x-polarization).
Far field function is (you will see later on):
Z
Y
Incremental electric
current
X

## Slide 15: BOR1 antennas
General form of far field function of BOR1 antenna with y-polarization:
E-plane pattern
H-plane pattern
Question: what are E-plane and H-plane?

## Slide 16: E-plane and H-plane
Define the radiation direction you are look into.
Then, we check all planes through this direction.
If there is such a plane that all E field vectors in far field on this plane lies in the plane, this plane is called E-plane.
The orthogonal plane to the E plane is called H plane because H vectors are orthogonal to E vector.
If there is no such plan for the antenna, then we say there is no E plane or H plane for this antenna.

## Slide 17: E-plane and H-plane (in practice)
For directional antenna, we usually put the maximum direction on z direction.
Then, we usually see XOZ and YOZ planes to see which is E plane and which is H plane.

## Slide 18: Examples of E-plane and H-plane
Z
Y
X
Incremental electric
current
E plane : YOZ
H plane : XOZ
E-plane pattern
H-plane pattern

## Slide 19: BOR1 antennas
General form of far field function of BOR1 antenna with y-polarization:
E-plane pattern
H-plane pattern
Note that
Do you know why?

## Slide 20: Characteristics of BOR1 antennas
Co- and cross-polar components of y-polarized BOR1 antenna:
where
Which are called as co- and cross-polar components
in 45 deg plane.
NOTE: valid only for BOR1 antenna
Notes: Show co pol vector

## Slide 21
The whole radiation pattern of BOR1 is defined by
  co- and cross-polar patterns in the 45 deg plane
  Or, E- and H-plane patterns.
Characteristics of BOR1 antennas

## Slide 22: BOR1 antenna: Circular polarization (RHC)
RHC co- and cross-polar patterns become:
where the same as before
Notes: Assum same BOR1 antenna along x and y axis

## Slide 23: BOR1 antenna: Power integral
Two alternatives:
φ-integration is ready done. Good!
Notes: Related to radiated power by P=2ηPrad

## Slide 24: Three widely used analytical expressions to represent pencil beam radiation patterns, either measured or simulated
Exponential:
Cosine:
Half cosine:
Best for presenting broad beams

## Slide 25: Directivity of BOR1 antenna with low sidelobes
When the antenna is y-polarized, the approximate far-field function:
The co-polar far-field function is
What is half 3dB beamwidth θ3dB?
Notes: Ge = Gh, Gxp=0. draw pattern to show half 3dB beamwidth.

## Slide 26: Directivity of BOR1 antenna with low sidelobes
The power integral is:
The directivity is
For small

## Slide 27: Directivity versus beam width
Half 3dB beam width
Half 10dB beam width
Half 20dB beam width

## Slide 28: Approximate formula: Directivity calculated by beam width even applicable to non BOR antenna
The directivity is
If the in E- and H-plane are different
We will use this in Lab 2

## Slide 29: System characterization Antenna gain (realized gain)
Antenna gain = total radiation efficiency * polarization efficiency * directivity

## Slide 30: System characterization Antenna gain (realized gain)
Radiation efficiency
where
Mismatch factor
Radiation efficiency

## Slide 31: System characterization Antenna gain (realized gain)
Polarization efficiency
G(0,0)
co
X
Y
Z

## Slide 32
D
c
o
q
j
,
(
)
(
)
d
B
i
10
G
c
o
q
j
,
(
)
2
G
I
S
O
2
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
è
ø
ç
÷
æ
ö
d
B
i
log
=
=
10
4
p
G
c
o
q
j
,
(
)
2
P
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
è
ø
ç
÷
æ
ö
d
B
i
log
Directive Gain of co-polar far field function:
Directivity (also for co-polar): maximum directive gain
Antenna gain
Notes: Note the difference maximun directivity and the maximun directive gain

## Slide 33: System characterization Aperture efficiency
Aperture area:
Maximum available directivity for large aperture A > l2 :
Aperture efficiency:
This is a very important equation in the book.
A
Notes: Not G0/Gmax=Ae/A

## Slide 34: System characterization Effective Area
Effective aperture:
Therefore,
Total power received at antenna port
Power density of the plane wave coming in

## Slide 35: System characterization : Antenna efficiency and Illustration of its subefficiencies

## Slide 36: Friis Transmission Equation
Power density:
Received power:
Friis Transmission equation:
(free space
attenuation)

## Slide 37: Radar Equation
Radar Equation:
Effective aperture:
RCS: Radar Cross Section

## Slide 38: System characterization Antenna noise temperature Tant
For receiving antenna, the actual figure of merit of communication or radar system is signal-to-noise ratio (SNR).
But in radio astronomy, it is often use equivalent noise temperature to describe the noise level.

## Slide 39: System characterization Physical source of noise
In 1906, Einstein predicted
  The fluctuating charges in a lossy resistor in thermal equilibrium would result in certain noise voltage at its terminals.
In 1928, this phenomenon was first observed by John B. Johnson and quantified by Harry Nyquist, both at Bell Labs.

## Slide 40: System characterization Physical source of noise
Bolzmann’s const.
Thermal noise is quantified as
Physical temperature of the resistor in Kelvins
Resistance.
voltage variance (mean square) per hertz of bandwidth

## Slide 41: System characterization Physical source of noise
A resistor in a short circuit dissipates a noise power
The maximum thermal noise Power output over a frequency band is
bandwidth

## Slide 42: System characterization Antenna noise temperature Tant
Then we can express all types of noise as they were from a resistor with a certain physical temperature
  equivalent noise temperature .
Tant is a measure of the received noise power Pn at the antenna port.
Bolzmann’s const.
bandwidth
Pnoise=KTantΔf
NOTE Tant is not the physical temperature of the antenna

## Slide 43: System characterization Figure of merit G/T
G/T is measured in dB/K.
Figure of merit:

## Slide 44: System characterization Antenna noise temperature Tant
-0.1 dB loss causes 7K increase in noise temperature at room temperature
Ambient temperature of antenna
Notes: Explain more. More accurate T0 should be Tant-physical

## Slide 45: System characterization Ta - Noise temperature from sky and ground
Brightness temperature in main beam direction
Ideal-antenna noise temperature (from sky & ground):
Brightness temperature
of sky Tb
Relative power hitting the ground
Ground temperature
Ambient temperature
Notes: Pgrd is the percentage of the power hitting the ground in the total radiated power

## Slide 46: System characterization Bandwidth
The characteristics of antennas are normally specified over a certain frequency band. Three common ways to present the bandwidth.
Bandwidth around the center frequency
Relative bandwidth
Ratio bandwidth
(for large bandwidth)

## Slide 47: Questions
What is the lowest brightness temperature of the sky and what is its origin?
  3 K, comes from Big Bang.
  Arno Penzias and Robert W. Wilson measured the temperature in 1960s and got Nobel prize.
There are some strong point sources of noise on the sky. Which is the strongest?
  The sun.

## Slide 48: The story of finding sky noise temperature
In 1965, Penzias and Wilson at Bell Labs
  were testing a very sensitive detector by pointing the instrument to sky,
  found that about 3K could not be explained by any reason
  concluded that the 3K is from outside the atmosphere
At the same time Bob Dicke and Jim Peebles at Princeton
  Suggested that the early universe be very hot, and glow white.
  We should still be able to see this glow since the light from very far away would just reach us now.
  Due to the Doppler phenomena, the light reaching us becomes microwaves. They were planning to do the measurements
When Penzias and Wilson heard of the Dicke&Peebles suggestion, they realized that they had found it, and they were awarded the Nobel Prize in 1978.
When Dicke and Peebles heard of Penzias&Wilson’s work, they realized that they missed the Nobel Prize.

## Slide 49: Learning goals of the Lecture
Definitions of BOR antennas
  antennas have completely rotationally symmetric geometry around one axis
Characteristics of BOR1 antennas
for y-polarized

## Slide 50: Learning goals of the Lecture
Antenna System Characterization
  Antenna gain
  Aperture efficiency
  Noise temperature
Calculate the noise temperature and G/T